## Slide 1
Agentic UAV Mission Planning and Safety Compliance Assistant
Agentic UAV Mission Planning & Safety Compliance Assistant
Abdul Azeem Hashmi • 2026

## Slide 2
Problem Statement
Manual UAV flight planning is slow, error-prone, and relies on expert knowledge. • Operators must verify airspace restrictions manually • No-fly zone violations risk collisions and regulatory penalties • Battery consumption is hard to predict without simulation • Compliance documentation is absent from most planning tools

## Slide 3
Agentic Solution Architecture
[>] 1. Mission Understanding Agent
Parses natural language using Google Gemini LLM -> structured JSON plan
[>] 2. Waypoint Planner Agent
Generates geometric paths: Square, Grid, Circle Orbit, Perimeter
[>] 3. Safety Compliance Agent
Enforces 7 rules: altitude, no-fly zones (line-segment checks), battery physics
[>] 4. Correction Agent
Normal-vector Shapely projection to nudge waypoints 15 m outside zones
[>] 5. Report Generation Agent
Exports PDF reports, CSV logs, QGC .plan files

## Slide 4
7 Safety Compliance Rules
[R1] Altitude <= 80 m
Prevents airspace intrusion & collision with manned aircraft
[R2] Takeoff waypoint present
Ensures mission begins at defined origin point
[R3] Landing/RTL waypoint
Guarantees safe terminal return command
[R4] Geofence clearance
Line-segment Shapely checks — no path crosses restricted zones
[R5] Leg <= 500 m
Limits single segment distance for signal reliability
[R6] Duration <= 30 min
Caps total operational flight window
[R7] Battery < 80% capacity
Physics model: climb 215W, cruise 120W, descent 115W, hover 130W

## Slide 5
Key Technical Innovations
[*] Haversine + Metric Projection
latlon_to_meters() converts lat/lon to local Cartesian metres for accurate Shapely geometry -- avoids degree-distortion at higher latitudes.
[*] Normal-Vector Correction Engine
Correction Agent projects violating waypoints to the zone boundary using Shapely's .boundary.project() + normal vector -> exact 15 m clearance.
[*] Physics-Based Battery Model
Multi-stage energy: Climb (215W @ 4 m/s), Cruise (120W @ 10 m/s), Descent (115W @ 2 m/s), Hover (130W) -- replaces heuristic estimate.
[*] QGroundControl (.plan) Export
Exports standard JSON .plan files with MAVLink commands directly importable into QGroundControl / PX4 autopilot.

## Slide 6
Live Demo Workflow
(1) Enter mission in natural language (e.g. 'Survey 500 m grid at 50 m altitude near 33.6N, 73.1E')
(2) Mission Understanding Agent parses intent -> structured JSON parameters
(3) Waypoint Planner generates flight path waypoints on interactive Folium map
(4) Safety Compliance Agent checks all 7 rules with physics models
(5) Correction Agent applies Shapely corrections if any rule fails
(6) Download PDF report, CSV log, and QGC .plan file with one click

## Slide 7
Results & Conclusion
[OK] All 7 safety rules enforced with physics-based validation [OK] Shapely line-segment geofence checks (not just point checks) [OK] Normal-vector boundary correction with exact 15 m clearance [OK] Multi-stage battery model replaces linear heuristic [OK] QGC .plan export for real controller compatibility [OK] 9 / 9 unit tests passing - Full documentation package Agentic UAV Mission Planning and Safety Compliance Assistant delivers a complete, safe, and deployable UAV mission planning system.
github.com/AbdulAzeemHashmi/agentic-uav-mission-planner